LABORATORY WORK NR. 5

Investigation of single-phase current rectifier

| Student. |  |  | Accomplished |  |
| --- | --- | --- | --- | --- |
|  | (group) |  |  | (date dėst. signature) |
|  |  | Defended |  |
| (name) |  |  | (date, dėst. signature) |

The objective - to learn about a variety of the rectifier structures, to investigate one-and two-side rectifiers, their filters, determine the characteristics of the rectifier.

Task - Investigate the various rectifiers with various filters, obtain the voltage curve U = f(t), an average values of rectified voltage, pulsations and filtration rates.

Equipment

1. Lab bench with generator and measuring devices KL-21001.

2. Basic electronic circuit experiment module KL-13007.

3. Measuring devices.

4. Wires.

5. Jumpers.

The workflow

1. Connect one side single diode rectifier circuit (Fig. 2.6).

Fig. 2.6 One side rectifier test circuit

- Work mode without a filter. For that  jumpers G, E and M are switched on . Connect the wires from the rectifier board KL-21001 to stand („AC SOURCE“ ~9 V ir 0 V). Connect a digital voltmeter, V and oscillograph.

- Turn on the voltage and copy adjusted voltage U = f(t) curve visible in the oscillograph screen (do not forget to draw the X-Y axis. X- axis must match with U=0 value, and only then copy it!).

- Measure the avarage adjuted voltage U0 with voltmeter V, Measure with oscillograph and write down the values in to the table 2.1. Calculate pulsation kp and filtration kf coefficients.

- Do the same for all rectifiers with filter working modes shown in the table:

- C filter - activated jumper L (connected capacitor C2)

- L filter - the jumpers is moved to G, C, and the coil (teacher will present) turned into selected location (L). Capacitor is disconected , remove jumper L.

- LC filter - return the jumper L.

- Resistace value R can be replaced by switching the jumper N.

kp1 - pulsation coefficients without filter (When only impedance is applied to load)

kp2 - filter rectifier pulsation coefficients (When connecting C, L, LC)

| Rectifier | One side |
| --- | --- |
| Resistivity R | R4=4,7 kΩ | R4+R5=2,35 kΩ |
| Filter | – | C | L | LC | – | C | L | LC |
| U0, V |  |  |  |  |  |  |  |  |
| ∆U, V |  |  |  |  |  |  |  |  |
| kp |  |  |  |  |  |  |  |  |
| kf | – |  |  |  | – |  |  |  |

Table 2.1 Rectifiers test and calcilation data.

5. Connect two-way rectifier circuit with diode bridge (Fig. 2.7)

Fig. 2.7 Two-way rectifier circuit with diode bridge

- Select rectifiers working mode without a filter. For that switch on jumpers A, B, C, D, G and M. Connect the wires from rectifiers board KL-21001 to stand („AC SOURCE“ ~9 V ir 0 V). Connect a digital voltmeter, V and oscillograph.

- Turn on the voltage and copy adjusted voltage U = f(t) curve visible in the oscillograph screen (do not forget to draw the X-Y axis. X- axis must match with U=0 value, and only then copy it!).

- Measure the avarage adjuted voltage U0 with voltmeter V, Measure with oscillograph and write down the values in to the table 2.2. Calculate pulsation kp and filtration kf coefficients.

- Do the same for all rectifiers with filter working modes shown in the table.

| Rectifier | Two-way |
| --- | --- |
| Resistivity R | R4=4,7 kΩ | R4+R5=2,35 kΩ |
| Filter | – | C | L | LC | – | C | L | LC |
| U0, V |  |  |  |  |  |  |  |  |
| ∆U, V |  |  |  |  |  |  |  |  |
| kp |  |  |  |  |  |  |  |  |
| kf | – |  |  |  | – |  |  |  |

Table 2.2 Rectifiers test and calcilation data.